Vicon T-Series Motion Capture System

The Vicon T-Series Motion Capture System is a series of specialized cameras with infrared lighting designed to track reflective markers in 3D space. Reflective markers are placed on any objects that wish to be captured. Each marker must be seen by at least three of the Vicon cameras in order to record its position. Cameras are placed on tripods in various heights and angles around the scene to be captured.

The T-Series cameras are capable of recording up to 1000 frames per second.

Cameras are attached via cables to a controller box, which in turn is connected via gigabit Ethernet to a Windows PC running the Vicon Tracker 2.0 software.

Calibrations are performed using a supplied T-shaped wand fit with 5 motion capture markers.

The Vicon Tracker 2.0 software allows setup and calibration of the cameras in the physical space, as well as grouping and identifying sets of markers. The software also records the data from the camera, displaying the markers or marker groups in a 3D space.

Pictures and info taken from http://www.vicon.com/